## Slide 1
Recap: Lecture 11: 4th Feb. 2014, 0830-0930 hrs.
  Equivalence of Kelvin-Planck statement and the Clausius statement
  Perpetual Motion Machines of the 2nd Kind
  Reversible and irreversible processes
  Causes of irreversibility
  Internal, external and totally reversible processes
  Carnot cycle
  Reversed Carnot cycle

## Slide 2
The Carnot cycle
The Carnot cycle consists of four reversible processes
  Two reversible adiabatic processes
  Two reversible isothermal processes
It can be executed in a closed system or a steady flow mode.
We shall consider a closed system consisting of a piston-cylinder arrangement.
Friction and other irreversibilities are assumed to be absent.

## Slide 3
The Carnot cycle
Reversible isothermal expansion (1-2)
Gas allowed to expand slowly.
Infinitesimal heat transfer to keep TH constant.
Since temperature differential never exceeds dT, reversible isothermal process.
Total heat transfer: QH
TH = constant
1
2
QH
Process 1-2
Energy
source
at TH

## Slide 4
The Carnot cycle
Reversible adiabatic expansion (2-3)
Insulation at the cylinder head
Temperature drops from TH to TL
Gas expands and does work
Process is therefore reversible and adiabatic.
TH
3
2
TL
Insulation
Process 2-3

## Slide 5
The Carnot cycle
3
4
Energy
sink
at TL
QL
TL = constant
Process 3-4
Reversible isothermal compression (3-4)
Insulation removed
TL is constant
Infinitesimal heat transfer to the sink at TL
Temperature differential never exceeds dT, reversible isothermal process
Total heat transfer: QL

## Slide 6
The Carnot cycle
Reversible adiabatic compression (4-1)
Temperature rises from TL to TH
Insulation put back
The gas is compressed in a reversible manner.
The temperature rises from TL to TH
TH
1
4
TL
Insulation
Process 4-1

## Slide 7
The Carnot cycle
1-2: A reversible isothermal process Q1=U2-U1 +W1-2
2-3: A reversible adiabatic process
0=U3-U2+W2-3
3-4: Reversible isothermal process
Q2=U4-U3-W3-4
4-1: Reversible adiabatic process
0=U1-U4-W4-1
Q1-Q2=W1-2+W2-3-(W3-4+W4-1)
Qnet= Wnet for the cycle

## Slide 8
The Carnot cycle
V
P
1
2
3
4
QH
QL
TH=constant
TL=constant
Wnet,out
S
T
1
2
3
4
QH
QL
TH=constant
TL=constant
P-V diagram of Carnot cycle
T-S diagram of Carnot cycle

## Slide 9
The Reversed Carnot cycle
The Carnot cycle comprises of reversible processes.
So all the processes can be reversed.
This is like a Carnot Refrigeration cycle.
The cycle remains same, but the directions of heat and work interactions are reversed.
QL : heat absorbed from the low temperature reservoir
QH : heat rejected to the high temperature reservoir
Wnet,in: Net work input required

## Slide 10
The Reversed Carnot cycle
V
P
1
2
3
4
QH
QL
TH=constant
TL=constant
Wnet,in
S
T
1
2
3
4
QH
QL
TH=constant
TL=constant
P-V diagram of Reversed Carnot cycle
T-S diagram of Reversed Carnot cycle

## Slide 11
The Carnot principles
There are theoretical limits to the operation of all cyclic devices (2nd law of thermodynamics).
Carnot principles:
  Efficiency of an irreversible heat engine is always less than that of a reversible engine operating between the same reservoirs.
  Efficiencies of all reversible heat engines operating between the same reservoirs are the same.

## Slide 12
Low temperature
Sink
The Carnot principles
High temperature
Source
HE 1
Irreversible
HE 2
Reversible
HE 3
Reversible
ηth,1 < ηth,2
ηth,1 < ηth,3
ηth,2 = ηth,3

## Slide 13
Low temperature
Sink, TL
Proof of the Carnot principles
High temperature
Source, TH
HE 1
Irreversible
HE 3
Reversible
Wnet,1
QH
QH
Wnet,2
QL,irrev<QL, rev
QL, rev

## Slide 14
Low temperature
Sink, TL
Proof of the Carnot principles
High temperature
Source, TH
HE 1
Irreversible
HE 3
Reversible
Wnet,1
QH
QH
QL,irrev<QL, rev
QL, rev
Wnet,2

## Slide 15
Low temperature
Sink, TL
Proof of the Carnot principles
HE 1
Irreversible
HE 3
Reversible
Wnet,1-Wnet,2
QH
QL,irrev
QL,rev
QH
The combined heat engine cycle generates a net work output while interacting with a single reservoir, violating the Kelvin-Planck statement.

## Slide 16
The thermodynamic temperature scale
A temperature scale that is independent of the properties of the substances that are used to measure temperature.
2nd Carnot principle: all reversible heat engines have the same thermal efficiency when operating between the same two reservoirs.
The efficiency of a reversible engine is independent of the working fluid employed and its properties, or the type of reversible engine used.

## Slide 17
The thermodynamic temperature scale
A temperature scale that is independent of the properties of the substances that are used to measure temperature.
We shall consider three reversible engines to derive an expression for f(TH,TL).

## Slide 18
The thermodynamic temperature scale
Low temperature
Sink, T3
High temperature
Source, T1
HE A
Q1
Q2
WA
HE B
HE C
Q3
Q1
Q3
WB
WC
T2

## Slide 19
The thermodynamic temperature scale
Since the LHS of the above equation depends only on T1 and T3, the RHS must be independent of T2

## Slide 20
The thermodynamic temperature scale
For this to be true,
In general, for a reversible engine,

## Slide 21
The thermodynamic temperature scale
Lord Kelvin proposed to define a
thermodynamic scale as
This is called the Kelvin scale and the
temperatures on this scale are called
absolute temperatures.
For reversible cycles, the heat transfer
ratio can be replaced by the absolute
temperature ratio.

## Slide 22
The thermodynamic temperature scale
On the Kelvin scale, the triple point of water was assigned a value of 273.16 K.
Therefore the magnitude of Kelvin is defined 1/273.16 K of the interval between absolute zero and the triple point of water.
Since reversible engines are not practical, other methods like constant volume ideal gas thermometers are used for defining temperature scales.

## Slide 23
The Carnot heat engine
A hypothetical engine that operates on the Carnot cycle.
We know that
Since the Carnot heat engine is reversible,
This is known as the Carnot efficiency and is the highest efficiency that a heat engine can have while operating between TH and TL (the temperatures are in Kelvin).

## Slide 24
Low temperature
Sink, 250 K
The Carnot heat engine
High temperature
Source, 1000 K
HE 1
Reversible
HE 2
Irreversible
HE 3
Imposssible
ηth<ηth,rev Irreversible heat engine
ηth=ηth,rev Reversible heat engine
ηth>ηth,rev Impossible heat engine
ηth=75%
ηth=55%
ηth=80%

## Slide 25
The Carnot heat engine
The efficiency of a Carnot heat engine increases as TH is increased, or as TL is decreased.
The thermal efficiency of actual heat engines can be maximized by supplying heat to the engine at the highest possible temperature and rejecting heat from the engine at the lowest possible temperature.

## Slide 26
Quality of energy
Low temperature
Sink, TL=300 K
High temperature
Source, TH
Reversible HE
Wnet
QH
QL
TH, K | ηth, %
1000 | 70
700 | 57.1
500 | 40
400 | 25
350 | 14.3

## Slide 27
Quality of energy
Energy has quality as well as quantity.
More of the high-temperature thermal energy can be converted to work.
The higher the temperature, the higher the quality of the energy.
Work is a high quality form of energy than heat since 100 percent of work can be converted to heat, but only a fraction of heat can be converted to work.