## Slide 1
Recap: Lecture 10: 3rd Feb 2013, 1130-1230 hrs.
  Kelvin-Planck statement of 2nd law of thermodynamics
  Refrigerators and heat pumps
  Coefficient of performance
  Clausius statement of 2nd law of thermodynamics

## Slide 2
Equivalence of the Kelvin-Planck and the Clausius statement
High temperature
reservoir at TH
Low temperature
Reservoir at TL
Refrigerator
QH+QL
QL
Heat Engine
QH
Wnet=QH
A refrigerator that works using a heat
engine with ηth=100%

## Slide 3
Equivalence of the Kelvin-Planck and the Clausius statement
High temperature
reservoir at TH
Low temperature
Reservoir at TL
Refrigerator
QL
QL
The equivalent refrigerator

## Slide 4
Perpetual motion machines of the second kind (PMM2)
Any device that violates the second law is called a perpetual-motion machine of the second kind (PMM2).
Such a device will
  Either generate work by exchanging heat with a single reservoir
  Or transfer heat from a low temperature reservoir to a higher temperature one without any work input.

## Slide 5
Pump
Perpetual motion machine of the second kind (PMM2)
Turbine
Pump
Boiler
System boundary
Qin
Wnet,out

## Slide 6
Reversible and irreversible processes
2nd law: no heat engine can have 100% efficiency
What is the highest efficiency that an engine could have?
Reversible process: a process that can be reversed without leaving any trace on the surroundings.
The system and the surroundings are returned to their initial states at the end of the reverse process.

## Slide 7
Reversible and irreversible processes
Reversible process: Net heat and work exchange between the system and surroundings (for original + reverse process) is zero.
Why reversible processes are of interest?
Consume least work in the case of work-consuming devices and generate maximum work in the case of work-producing devices.

## Slide 8
Reversible and irreversible processes
Reversible processes serve as theoretical limits for the corresponding irreversible ones.
Reversible processes leads to the definition of the second law efficiency for actual processes, which is the degree of approximation to the corresponding reversible processes.

## Slide 9
Irreversibilities
Commonly encountered causes of irreversibilities
  friction, unrestrained expansion, mixing of two fluids, heat transfer across a finite temperature difference, electric resistance, inelastic deformation of solids, and chemical reactions.

## Slide 10
Irreversibilities
30oC
10oC
30oC
Heat
Heat transfer through a finite temperature difference is irreversible.
10oC
5oC
30oC
Heat

## Slide 11
Irreversibilities
800 kPa
25 kPa
Fast compression
Fast expansion
Unrestrained expansion

## Slide 12
Internally and Externally Reversible Processes
Internally reversible process
  if no irreversibilities occur within the boundaries of the system during the process.
  the paths of the forward and reverse processes coincide for an internally reversible process

## Slide 13
Internally and Externally Reversible Processes
Externally reversible process
  no irreversibilities occur outside the system boundaries during the process.
  Heat transfer between a reservoir and a system is an externally reversible process if the outer surface of the system is at the temperature of the reservoir.
Totally reversible or reversible
  no irreversibilities within the system or its surroundings.

## Slide 14
Internally and Externally Reversible Processes
Heat
35oC
Thermal energy
reservoir at 35.000001o C
Heat
35oC
Thermal energy
reservoir at 45o C
Boundary
at 35o C
(a) Totally reversible
(b) Internally reversible

## Slide 15
Reversible adiabatics
Two reversible adiabatic paths cannot intersect
Through one point, only one reversible adiabatic can pass
Violation of Kelvin-Planck statement
P
v
A
B
C
Reversible
isotherm
Reversible
adiabatics

## Slide 16
Reversible adiabatics
Process m-n
Qm-n = Un –Um +Wmn
Process m-a-b-n
Qm-a-b-n=Un –Um+Wm-a-b-n
Since, Wm-a-b-n = Wmn
Qm-n = Qm-a-b-n
= Qm-a+ Qa-b + Qb-n
Since Qm-a = 0, Qb-n = 0
Qm-n = Qa-b
P
v
m
n
b
Reversible
isotherm
Reversible
adiabatics
a
Reversible path can be substituted by two reversible adiabatics and a reversible isotherm

## Slide 17
The Carnot cycle
The cycle efficiency can be maximised by using reversible processes.
Reversible cycles cannot be achieved in practice because the irreversibilities.
Reversible cycles provide upper limits on the performance of real cycles.
The Carnot cycle, proposed in 1824 by Sadi Carnot, is a reversible cycle.
The theoretical heat engine that operates on the Carnot cycle is called the Carnot heat engine.

## Slide 18
The Carnot cycle
The Carnot cycle consists of four reversible processes
  Two reversible adiabatic processes
  Two reversible isothermal processes
It can be executed in a closed system or a steady flow mode.
We shall consider a closed system consisting of a piston-cylinder arrangement.
Friction and other irreversibilities are assumed to be absent.

## Slide 19
The Carnot cycle
Reversible isothermal expansion (1-2)
Gas allowed to expand slowly.
Infinitesimal heat transfer to keep TH constant.
Since temperature differential never exceeds dT, reversible isothermal process.
Total heat transfer: QH
TH = constant
1
2
QH
Process 1-2
Energy
source
at TH

## Slide 20
The Carnot cycle
Reversible adiabatic expansion (2-3)
Insulation at the cylinder head
Temperature drops from TH to TL
Gas expands and does work
Process is therefore reversible and adiabatic.
TH
3
2
TL
Insulation
Process 2-3

## Slide 21
The Carnot cycle
3
4
Energy
sink
at TL
QL
TL = constant
Process 3-4
Reversible isothermal compression (3-4)
Insulation removed
TL is constant
Infinitesimal heat transfer to the sink at TL
Temperature differential never exceeds dT, reversible isothermal process
Total heat transfer: QL

## Slide 22
The Carnot cycle
Reversible adiabatic compression (4-1)
Temperature rises from TL to TH
Insulation put back
The gas is compressed in a reversible manner.
The temperature rises from TL to TH
TH
1
4
TL
Insulation
Process 4-1

## Slide 23
The Carnot cycle
1-2: A reversible isothermal process Q1=U2-U1 +W1-2
2-3: A reversible adiabatic process
0=U3-U2+W2-3
3-4: Reversible isothermal process
Q2=U4-U3-W3-4
4-1: Reversible adiabatic process
0=U1-U4-W4-1
Q1-Q2=W1-2+W2-3-(W3-4+W4-1)
Qnet= Wnet for the cycle

## Slide 24
The Carnot cycle
V
P
1
2
3
4
QH
QL
TH=constant
TL=constant
Wnet,out
S
T
1
2
3
4
QH
QL
TH=constant
TL=constant
P-V diagram of Carnot cycle
T-S diagram of Carnot cycle

## Slide 25
The Reversed Carnot cycle
The Carnot cycle comprises of reversible processes.
So all the processes can be reversed.
This is like a Carnot Refrigeration cycle.
The cycle remains same, but the directions of heat and work interactions are reversed.
QL : heat absorbed from the low temperature reservoir
QH : heat rejected to the high temperature reservoir
Wnet,in: Net work input required

## Slide 26
The Reversed Carnot cycle
V
P
1
2
3
4
QH
QL
TH=constant
TL=constant
Wnet,in
S
T
1
2
3
4
QH
QL
TH=constant
TL=constant
P-V diagram of Reversed Carnot cycle
T-S diagram of Reversed Carnot cycle