## Slide 1
Recap: Lecture 5: 16th January 2014, 0930-1025 hrs.
  Joule’s experiment
  Work
    Types of work
    Displacement work
    Displacement work for different processes
  First law of thermodynamics
    Energy balance
    Energy change of a system
    Energy transfer mechanisms

## Slide 2: Heat
Thermodynamic definition of heat:
When a system whose surroundings are at a different temperature and on which work may be done undergoes a process.
The energy transferred by non-mechanical means, equals to the diference between the internal energy change and the work done is called heat.
It took many years before it was understood that heat is energy
  First really conclusive evidence that heat could not be substance was given by Benjamin Thompson from Messachusetts who later became Count Rumsford
  In 1798, Rumsford observed the temperature rise in the brass chips produced during the boring of cannon and concluded that work on boring was responsible for the flow of heat.

## Slide 3: Heat
One year later Sir Humphry Devy tried to prove the point by showing that two pieces of ice could melt if they are rubbed together
His idea was to show that heat is a manifestation of energy but his experiment was highly inconclusive.
Seguin (a French engineer) in 1839 and Mayer (German Physician) in 1842 tried unsuccessfully to prove the point.
Experiments of Joule between 1840-1849 in a private laboratory were able to convince the world through a series of experiments
  Showed the relation between heat and work once and for all and showed the equivalence between the two quantities
  Helmholtz wrote a brilliant paper in 1847 on Joule’s experiments and applied these ideas for physical chemistry and physiology.

## Slide 4: Concept of Heat
Heat is internal energy in transit
  Flowing from a part of the system to another
  or from one system to another
  By virtue of only a temperature difference
  Heat transfer can be determined only when time t2 – t1 is known
  It is incorrect to say that heat is in the body
    Or work in the body
  The performance of work and flow of heat are methods whereby the internal energy of a system is changed
  It is impossible to separate or divide the internal energy into mechanical and thermal part.

## Slide 5
First law for a cycle
For a closed system undergoing a cycle, the initial and final states are identical.
Therefore, ΔEsystem= E2 - E1 = 0
The energy balance for a cycle simplifies to
Ein - Eout = 0 or Ein = Eout

## Slide 6
First law for a cycle
A closed system does not involve any mass flow across its boundaries, the energy balance for a cycle can be expressed in terms of heat and work interactions as

## Slide 7
First law for a cycle
Qnet = Wnet
P
V
For a cycle, ΔE = 0, thus Qnet = Wnet

## Slide 8
In processes involving a change of state, heat and work interactions may be unknown.
It is a usual practice to assume the direction of heat and work interactions.
It is usually assumed that heat to be transferred into the system (heat input) in the amount of Q and work to be done by the system (work output) in the amount of W.
First law for a system undergoing a change of state

## Slide 9
First law for a system undergoing a change of state
The energy balance would be:
Obtaining a negative quantity for Q or W simply means that the assumed direction for that quantity is wrong and should be reversed.

## Slide 10
First law for a system undergoing a change of state
System
System
Surroundings
Q
Q3
Q2
Q1
W
W1
W2
W4
W3

## Slide 11
First law for closed systems

## Slide 12
First law: isolated system
An isolated system has no interaction between the system and its surroundings
For an isolated system, đQ=0 and đW=0
The first law gives
dE=0
or, E=constant
The energy of an isolated system is thus, always a constant.

## Slide 13
First law : some observations
The first law cannot be proven mathematically, but no process in nature is known to have violated the first law.
First law of thermodynamics is a fundamental physical law in itself.
From the first-law point of view, heat and work are not different at all.
However heat and work are very different from the second law point of view.

## Slide 14
Perpetual Motion Machine of the First Kind (PMM1)
Any device that violates first law is called a perpetual-motion machine of the first kind (PMM1).
Such a device will create energy!
Numerous ideas have been proposed over the years, of various devices that generate energy in some way.
These devices of course violate the first law and hence were never demonstrated.

## Slide 15
Pump
Perpetual Motion Machine of the First Kind (PMM1)
Condenser
Turbine
Generator
Pump
Boiler
Resistance heater
System boundary

## Slide 16
Perpetual Motion Machine of the First Kind (PMM1)
The device continuously produces energy at a rate of without receiving any energy.
This is a clear violation of the first law.
Converse of a PMM1: there can be no machine which would continuously consume work without some other form of energy appearing simultaneously.