## Slide 1
Recap: Lecture 6: 20th January 2014, 1130-1230 hrs.
  First law for a cycle
  First law for a system undergoing a change of state
  First law for an isolated system
  Perpetual Motion Machines of the First Kind (PMM1)

## Slide 2
First law of thermodynamics for open systems
First law process applied to flow process
  System approach: Lagrangian
  Control volume approach: Eulerian
Steady flow processes
Unsteady flow processes

## Slide 3
First law of thermodynamics for open systems
Steady flow processes: rates of flow of mass, energy are constant across the system boundary
  eg. Turbines, compressors, heat exchangers etc
Unsteady flow processes: rates of mass, energy are not constant across the system boundary
  eg. Charging and discharging process (tanks, pipelines etc.)

## Slide 4
Conservation of mass
Conservation of mass principle
  Total mass entering the system - Total mass leaving the system = Net change in mass within the system

## Slide 5
Flow work and the energy of a flowing fluid
Work required to push the mass into or out of the control volume: flow work or flow energy.
Consider a fluid element of volume V.
Let fluid pressure be P, the cross-sectional area be A, L is the distance through which the imaginary piston must move.
The work done in pushing the fluid element across the system boundary is
Wflow = FL = PAL = PV

## Slide 6
Flow work and the energy of a flowing fluid
CV
V
P
m
A
L
F
Imaginary
piston

## Slide 7
Total energy of a flowing fluid
The fluid entering or leaving a control volume possesses an additional form of energy—the flow energy, Pv
The total energy of a flowing fluid on a unit-mass basis (denoted by θ) becomes
θ = e + Pv= (u + ke + pe) + Pv
Since u+Pv=h,
  θ = h + ke + pe (kJ/kg)
Therefore, enthalpy, h, takes care of the flow work in addition to the internal energy.

## Slide 8
Total energy of a flowing fluid
The total energy consists of three parts for a non flowing fluid and four parts for a flowing fluid.

## Slide 9
Energy transport by mass
θ is total energy per unit mass, the total energy of a flowing fluid of mass m is simply mθ, for uniform properties of the mass m.

## Slide 10
Energy analysis of steady flow systems
Several engineering devices can be approximated to operate as steady flow devices: turbine, compressors, nozzles etc.
During a steady-flow process, no intensive or extensive properties within the control volume change with time.
The boundary work is zero for steady-flow systems (since VCV =constant).
The total mass or energy entering the control volume must be equal to the total mass or energy leaving it.

## Slide 11
Energy analysis of steady flow systems
Properties of steady flow processes
  No properties within the control volume change with time.
  No properties change at the boundaries of the CV with time.
  The rates of flow of energy and mass across the control surface is constant.
  Thermodynamic property has a fixed value at a particular location and do not change with time.

## Slide 12
Energy analysis of steady flow systems
mCV=constant
ECV=constant
Mass in
Mass out
Control
volume
mCV=constant
ECV=constant
Control
volume
Under steady-flow conditions, the fluid properties at an inlet or exit remain constant (do not change with time).

## Slide 13
Energy analysis of steady flow systems
For a steady flow system, the amount of energy entering a control volume in all forms (by heat, work, and mass) must be equal to the amount of energy leaving it.
Energy balance for a steady flow system
=0

## Slide 14
Energy analysis of steady flow systems
Energy balance for a steady flow system written more explicitly,

## Slide 15
Energy analysis of steady flow systems
The energy equation is also written as:

## Slide 16
Energy analysis of steady flow systems
For single entry and exit devices,

## Slide 17
Steady flow energy equation for common engineering devices
Some commonly used steady flow engineering devices:
  Nozzles and diffusers
  Compressors and turbines
  Throttling devices
  Mixing chambers
  Heat exchangers

## Slide 18
Nozzles and diffusers
A nozzle is a device that increases the velocity of a fluid at the expense of pressure.
A diffuser is a device that increases the pressure of a fluid by slowing it down.
The cross-sectional area of a nozzle decreases in the flow direction for subsonic flows and increases for supersonic flows. The reverse is true for diffusers.

## Slide 19
Nozzles and diffusers
Nozzle
Diffuser
V1
V1
V2>>V1
V2<<V1
Nozzles and diffusers are shaped so that they cause large changes in fluid velocities and thus kinetic energies.

## Slide 20
Nozzles and diffusers

## Slide 21
Turbines and compressors
Pumps, compressors and fans: used to increase the pressure of a fluid and require work input.
Turbines generate work.
Q, KE and PE may or may not be zero.
Usually PE is negligibly small.

## Slide 22
Turbines and compressors
Turbine
WT
1
2
Control surface
Insulation

## Slide 23
Turbines and compressors
For a turbine for eg., the energy equation would be:

## Slide 24
Throttling device
Throttling valves are any kind of flow-restricting devices that cause a significant pressure drop in the fluid.
Eg: capillary tubes, valves
Unlike turbines, they produce a pressure drop without involving any work.
The pressure drop in the fluid is often accompanied by a large drop in temperature.
Hence throttling devices are commonly used in refrigeration and air-conditioning applications.

## Slide 25
Throttling device
An adjustable valve
A porous plug
A capillary tube

## Slide 26
Throttling device

## Slide 27
Throttling device

## Slide 28
Throttling device
u1=87.46 kJ/kg
P1v1= 1.1 kJ/kg
(h1 = 88.56 kJ/kg)
u2=72.32 kJ/kg
P2v2= 16.24 kJ/kg
(h2 = 88.56 kJ/kg)
During a throttling process, the enthalpy (flow energy + internal energy) of a fluid remains constant. But internal and flow energies inter-convertible.

## Slide 29
Mixing chambers
The section where the mixing process takes place is commonly referred to as a mixing chamber.
Eg.: mixing of hot and cold water at the T joint of a shower.